## Slide 1: Using MMDS Surplus Amplifiers For 2304
MMDS Amplifiers re-tuned to 2034
And
Control Circuit Ideas
Gary
WA2OMY

## Slide 2: Two Types of Surplus MMDS Transmitters
ITS Transmitter
EMCEE Transmitter
Exciter

## Slide 3: ITS TRANSMITTERS
ITS Transmitter driver - spare 12 W amplifier
Used in Feedforward amp design, not needed for xmit amp after conversion.
Requires:
  -5V Bias @ 130 mA
  10V Drain Supply @ 5.2 A
  (12V w/ 2 diode drop)

## Slide 4: EMCEE Transmitters
  Driver amplifier- 2 stages
  4 amps in ea. chassis
    2- driver
    2- 10 W stage
    2 Complete amplifiers if 2 stages used.
    Requires -
    -15 V Bias w/ on-board
    -5 V zener
    +12V w/ on-board series
    resistor for
    drain supply of 10V.

## Slide 5: EMCEE Amplifiers Retuned 2304
Enough gain for 11 W from mixer-filter
1st 2 stages of driver MMIC design.
Remove one for less gain

## Slide 6: All Amplifiers based on Fujitsu FLL200 -3 GaAs FET

## Slide 7: 2304 Amplifiers

## Slide 8: What do we need for easy amateur use?
Built in -5 V supply
TR Switch control
Bias protection
Drain Current monitor (Nice to have)

## Slide 9: Negative Bias supply
Linear Tech - LT1931 Inverting DC-DC converter
Low noise- Low ripple – 1 MHz switching Frequency
Easy to use
1st – Breadboard of – V switching supply
Linear Tech suggested application schematic. (Just what we need)

## Slide 10: TR Control
W6PQL – High Current DC Fet Switch

## Slide 11: Bias Protection
Modify W6PQL FET Switch
- Add FET for bias protection

## Slide 12
Final Prototype Circuit to control FET amplifiers
-5V Supply, W6PQL FET SW, Drain Current monitor
-5V supply
Bias Protection
Drain current
monitor

## Slide 13
Prototype of complete 14W amplifier from ITS Chassis
12 V IN
Gnd to turn on amplifier (Pushbutton- for test)

## Slide 14: PCB 123 Boards

## Slide 15: PWB in Sunstone Circuits
Schematic and PL in PCB123
    (Sunstone Circuits)
Amplifiers available
Boards – kits available- depending on interest

## Slide 16: Next steps
Make controller for high power stages
ITS Transmitters 50W
EMCEE transmitters 2- 30 W amplifiers.