## Slide 1: Rights & Permission
  This presentation was created by Wayne Getchell of Sagacitic Solutions, amateur radio callsign VE3CZO. It is meant for reference use. Do not copy or publish it without permission and citation. If asked, permission is easily obtained for not for profit use. Send your request to Wayne at getch@sagacitic.com. If you want to use any part or all of it for profit let’s talk.

## Slide 2
Wayne Getchell VE3CZO
Software Description
Battery Monitor

## Slide 3: Software Overview
Summary
  Calculates then displays six values on a 16x2 line display
    Source Voltage - Load Current - Load Power
    Battery Use in Ah or Wh - Session Time - % remaining battery capacity
  Measurements are made and the display updated 10,000 times per hour or every 360mS (2.8 times per second)
    Measurement interval makes battery use accumulation easy
  Utilities Menu items to manage device
    Look at and erase Vmin & ILpeak - Clear readings
    Choose Ah/Wh display - Set Backlight - Select Battery
    Hibernate - Power Off - Calibration

## Slide 4: Software Overview
Objectives
  Accurate arithmetic results – calculations done to at least the display resolution often better
  Accumulate Ah / Wh accurately
    Precise timing loop to achieve 10k samples per hour
  Utilities menu as easy to navigate as possible with the two switches available

## Slide 5: Software Architecture
Measure
Utility Subs
Utilities
Sw Pressed?
Yes <2sec
No
Hibernate / PwrOff
Initialize
Yes >2sec

## Slide 6: Memory Use
External EPROM
  26 bytes of 256 stores housekeeping data
    HibernateState - Hours - Clock - nAh - mAh - Ah
    uWh - mWh - Wh - AhWh - Vbattmin -ILmax
    Tick - Sf - Battery - Display backlight level
20X2 Internal Memory
  EEPROM 256 bytes used to stores up to 8 batteries each battery uses 32 bytes (6 batteries pre-loaded)
  Scratchpad RAM – all 128 bytes used for battery terminal voltage versus % remaining capacity
  SFR User RAM
    $0-$37 56 bytes variables b0-b55
    $3c-$51 21 bytes for display data
    $40-$4d 14 bytes for LoadBatteryCap subroutine

## Slide 7: Initialization
  Set processor speed to 4MHz
  Configure processor output switches (5)
  Configure I2C display & display splash screen
  Write special characters to the display
  Configure processor A/D converter
  Load configuration data from external EEPROM
  Check Tick & Sf values use defaults if outside limits
  Load battery cap % remaining lookup table into scratchpad
  Pause to allow time to read splash screen
  Check if unit is returning from hibernation if so display ‘Resuming from Hibernation’ if not then clear readings
  Define gain range as 2 consistent with the processor switches then execute auto gain range twice to get current to voltage converter ready for first measurement

## Slide 8: Main Measuring Loop
Check Vsmin
Gain Autorange
Measure Vsource
Measure ILoad
Check ILmax
Calc Load Power
Update Time
Estimate Batt Cap
Gain Autorange
Inc Clock
Calc Ah/Wh
Pause to Interrupt
Write Display
Interrupt Routine
Enable interrupts
Reset Timers

## Slide 9: Measuring Loop Timing
Load Current Measurement
Cycle Start
Time (mS)
0
1st Gain Autorange
2nd Gain Autorange
32
85
210
Main Loop Pause Starts
260
Int Sub Begins
330
360
End Cycle

## Slide 10: Vsource & ILoad
Source Voltage
  Read 6:1 voltage divider A-D multiply by 6 & round result
  Convert to ASCII and store in SFR
Load Current
  Read voltage to current A-D. Scale the reading by multiplying by the Sf (valid range +/- 10%). Store as ILraw
  Calculate IL from ILraw & GainRange
    GainRange1*ILraw, 1, GR1=10ILraw, GR2=40ILraw
  Round result and convert to ASCII for display.
  Format depending on value for xxxmA x.xxA or xx.xA
  Store in SFR

## Slide 11: GainAutorange & Load Power
GainAutorange
  Selects one of three ranges for the current sense to voltage converter
  A-D converter value is used to determine whether to increase gain, decrease gain, or keep it the same
LoadPower
  Multiplies IL*Vsource As IL can be >40,000 and Vsource up to 246 (24.6V) product can easily overflow
  IL divided into 5 ranges to optimize product resolution while insuring product doesn’t overflow
    Calculations assume max voltage 246
    IL<267, <1331(/5/2), <5321(/20/5), <=26,600(/100/1) >26,600(/200/5)
    Each range is formatted for display depending on product result as x.xxW xx.xW xxxW or XxxxW (1,107W max)

## Slide 12: Elapsed Time & Batt Cap
Elapsed Time
  Time based on 10,000 cycles per hr, clock reg increments each cycle, hrs register increments every 10,000
  Minutes calculated as clock*6/1000 not rounded
  Time displayed in HH:mm format to 99:59
BattCapLeft
  Displays estimate of remaining battery capacity in xx%
  LoadBatteryCap sub populated scratchpad with table representing 0,2,5,10,20,30,40,50,60,70,80,90,99% capacity based on battery data stored in EEPROM
  Scratchpad get using source voltage as address returns % capacity
  Battery terminal voltage 5.2 to 17.9= addresses 52 to 51
  Numbers below 52 = 0% and above 179 = 99%

## Slide 13: Ah and Wh
Amp Hours
  Base unit is 10^-4hrs*10^-3A=10^-7Ah 10,000nAh=1mAh
  Accumulates by adding IL in mA to previous nAh reading each cycle. If nAh>=10,000 add to mAh reg, if mAh>=1000 add to Ah reg. Accumulates to 9999Ah
  Display format reads xxxmAh, x.xxAh, xx.xAh or XxxxAh
Watt Hours
  More complex, can’t just use mW over time like Ah, number is too big max >10^6mW so divide in to ranges
  Base unit is 10^-4hrs*10^-3A*10^-1V=10^-8Wh
  To keep below 65K limit code symbols uWh=10^-8Wh, mWh=10^-4Wh so it takes 10,000mWh to make a Wh.

## Slide 14: Ah and Wh (cont’d)
Watt Hours
  To prevent multiplication overflow calculation is broken up into 5 ranges so that Vsource*IL+ accumulated uWh<65k
  Like Watts each range assumes maximum Vsource=246
  Range 1 IL<=225 max = 225*246+9999=65349uW
  Range 2 IL between 226 & 1290. Calc de-normalizes uWh to uWh/5. IL/5*Vsouce+uWh/5 =1290/5*246*9999/5=65476 Now additional mW=uWh/2000+mWh (not 10,000) Remaining uW are calculated & normalized uW=uW//2000*5
  Similarly ranges 3 to 5 divide uWh & IL by 20,100,200
  Accumulates to 9999Wh using registers for uWh, mWh, Wh
  Display format reads xxxmWh, x.xxWh, xx.xWh or XxxxWh

## Slide 15: Utilities
Utility Management Routine
  Displays and allows user to select menu items
Eight utilities subroutines
  Min And Peak Clear Readings ChooseAhWh
  SetBacklight SelectBattery GoHibernate
  PowerOff Calibration
Other Subroutines
  WaitForSwitch StartNewReadings SetBacklightLevel
  RoundIt Decimal LoadBatteryCap

## Slide 16: Battery Data Storage
Uses all 20X2 EEPROM
  Up to eight sets of data for eight different batteries
  Base code populated with 3 & 6 cell lead acid, 10 & 11 cell NiMH and 3 & 4 cell LiPo.
  Data stored in two 16 byte ‘lines’ a battery occupies 32bytes
  First 16 bytes are a description of the battery 15bytes used
  Second 16 bytes stores battery terminal voltage representing 2,5,10,20,30,40,50,60,70,80,90 & 99% capacity.
    Three digits for each entry, xxx represents xx.x volts.
    If under 10.0V the leading zero must be present
  'Battery0
  EEPROM $00,("3 Cell LeadAcid")
  EEPROM $10,(053,054,055,056,057,058,059,060,061,062,063,064)

## Slide 17: BatteryMonitor Challenges
Creating new ways to do things
  Optimizing calculations - Sf - Watts - Wh -Time
Making code more efficient
  Ran out of space several times
  Found several ways to do same thing some more code efficient
  Documented learning
PICAXE bugs
  A-D positive reference bug
  I2C writes in interrupt timing loop create code execution instability