## Slide 1: Finding sites with Heywhatsthat
Rene Barbeau
VE2UG. 2018

## Slide 2: The need
Operating from home is difficult if not impossible
Portable operation is more flexible technically
10 GHz operation is a good start, not limited to LOS (Line of Sight) in our experience
LOS is mandatory for higher bands, except for the better stations on 24 GHz

## Slide 3: The need
Short LOS hops are easy to find, longer path need more work
Once prospective sites are found landmarks are needed to point the dish. Especially on higher bands where no beacons are available
Is there an easy, intuitive solution ?
Enter Heywhatsthat

## Slide 4: Heywhatsthat
Suggested by Mike N1JEZ who uses the application
Heywhatsthat is a website that provides synthetic panoramas from a location (www.heywhatsthat.com)
Used by sightseers, hikers to identify landmarks
It has various tools, usable for Hams

## Slide 5: 4 main modules
Panorama
Visibility cloak
Horizon
Path Profiler

## Slide 6: Panorama
Used by most users
For Hams, gives a general view of the landscape. When combined with Path Profiler it gives an aiming point to the other station

## Slide 7: Visibility cloak
Shows the terrain visible (LOS) from a hilltop, or any other site
Based on Google Maps
Potential sites are easily spotted
Has been known to work up to 215 km (Whiteface - Mt Tremblant)

## Slide 8: Horizon
Shows the maximum distance visible (LOS) from a hilltop
Easy to spot farthest possible sites
Those sites may not be accessible by usual means

## Slide 9: Path Profiler
To get a view of the path between stations
Based on Google Maps
If obstructed you can point and click on an obstruction to see where it is located
On non-LOS paths one can evaluate the effect of knife edge, or tropo horizon (like Whiteface to FN47 on the St-Laurence Valley)

## Slide 10: How it works
Enter Heywhatsthat website
Click on « New Panorama »
Enter data or click on map
Get result. Click on « Visibility Cloak » and « Horizon »
Zoom and survey map to find potential sites. Click site to see Path Profiler results
Tweak data in path profiler« Parameters »
http://www.heywhatsthat.com/techfaq.html

## Slide 11: Entering data

## Slide 12: Entering data

## Slide 13: Results -> Panorama

## Slide 14: Result -> Visibility cloak + Horizon

## Slide 15: Result -> Visibility cloak + horizon to Tremblant

## Slide 16: Evaluation with Path profiler
Entering new site by clicking on map
Edit parameters Menu. 0.14 is visual refraction (see techfaq)

## Slide 17: Path Profiler result with Tremblant

## Slide 18: Path profiler results with Lancaster

## Slide 19: Path Profiler result with St-Hilaire

## Slide 20: Path Profiler with FN47

## Slide 21: Site Survey Tips
Finding a site is one thing. But is it usable ?
If possible use Google Street View before leaving !
Do a printscreen of the Path Line, for reference in the field
Be prepared for the worst (trees). I hate trees

## Slide 22: Trees or else
FN24, LOS from Whiteface. Humm..

## Slide 23: Trees or else
FN35 top of hill. Where do I setup ?

## Slide 24: Trees or else
Even one tree is enough..(FN47)

## Slide 25: Google Street View Ottawa

## Slide 26: Path Line Whiteface vs Ottawa
We can use parking lines for heading

## Slide 27: Path Line Tremblant vs FN24

## Slide 28: Path Line Whiteface vs St-Hilaire

## Slide 29: Path Line Whiteface vs FN47

## Slide 30: 2015 season
47 GHz. Granby site, 148 Km. Copied Henry KT1J on Whiteface with a bare mixer. No QSO
47 GHz. Venise-en-Quebec site near the border. No QSO due to pointing error and frequency uncertainty

## Slide 31: 2016 season
10 GHz. St-Hilaire site to Whiteface. 59++
24, 47 GHz. Lancaster site to Whiteface 99 Km. 59++
24, 47 GHz. Tremblant site to Whiteface 215 Km. 51 and 339

## Slide 32: 2017 season
Survey work FN35 to Whiteface (Trees)
10, 47 GHz, FN35. Better site near St-Hilaire (Title picture). 59
10 GHz, Huron belvedere, King Mt sites near Ottawa
47 GHz, FN24 to Whiteface. 59+
10 GHz. FN24 site to Tremblant. 59
144, 222, 1296. FN47 to Whiteface
78 GHz. Site near the border to Champlain and St-Albans. 59

## Slide 33: And 2018
10 GHz and up. Site on Mt-Royal to Whiteface, St-Albans
More to come !

## Slide 34: Conclusions
A great tool to find new sites and spur local activity
Way to engage small groups to work between contests. Hone skills, more points
Help to push limits at millimeter frequencies. List of sites to extend distances as skills improve
And you found the perfect reason to buy that PA/LNA or high end transverter…

## Slide 35: Special Thanks
Thanks to the group who made all this possible. It was fun! 
Mike N1JEZ
Ray VE3FN
Henry KT1J
Paul W1GHZ
Luc VE3LUP
Glenn VE3XRA
Dean VE3CDD

## Slide 36
Questions?