## Slide 1: PCOM RX Mixer Hacks
Rene Barbeau
VE2UG. 2018

## Slide 2: How it started
Needed a test source at 78 GHz!
Found that a PCOM RX mixer have output as is. Bias port not used
Work at 78 GHz. Other frequencies?
And what about using it as a transverter?
Let’s try!

## Slide 3: PCOM RX Mixer Mods
3 ports, WR28, SMA for LO and RX IF
3 DC lines. Bias (0 to 10V), supplies to RX IF amp (+12V and -5V)
Remove RX IF amp to make bi-directionnal port
2 tests, source and transverter
Tests at 24, 47, 78, 122 and 134 GHz
Be bold, try 241 GHz too! Lets see if we have something

## Slide 4: Test Bench

## Slide 5: As a source
See output up to 134 GHz. 241 don’t pass Manual Signal ID Test.
Adjust bias for max output
Bias setting could change with load presented to WR28 port
Look in the Proceedings for all the traces

## Slide 6: As a source, best at 47 GHz

## Slide 7: Some output at 134 GHz

## Slide 8: As a transverter
It works! Confirmed TX and RX at 78 GHz. See output at 24, 47, 122, 134 and even 241 GHz
122 GHz and above need output confirmation with on-the-air tests
Adjust bias for max output
Bias setting could change with load presented to WR28 port

## Slide 9: As a transverter
Like similar designs, need a RX preamp
Output at 122 GHz is surprising
Look in the Proceedings for all the traces

## Slide 10: 122 GHz transverter output

## Slide 11: 241 GHz transverter output

## Slide 12: PCOM vs DB6NT MKU 47 G
20 dB less compared with DB6NT
As a source PCOM has similar output
Pair the PCOM with a ZLPLL 14G and you have a basic multiband rig
Can be used as a bench signal source
Also good for minimum >1 km QSO with simple antenna
Can hike your total in contests!

## Slide 13
Questions?