## Slide 1
Surface Mount Assembly
with a Toaster Oven
Mike Seguin, N1JEZ
Eastern VHF/UHF/Microwave Conference 2024

## Slide 2
The Problem
New/interesting parts are getting smaller
Some no longer have leads that are easy to solder
They now have pads on the underside of the package
And can have a ground pad on the underside as well Pad can be tied to the die for Thermal management
Enter the Toaster Oven!
But how to make it work?

## Slide 3
Kester EP256 Lead Solder Paste
63/37 Syringe Dispenser
Refrigerate when not in use

## Slide 6
RefloLeo is a KickStarter project
Arduino Leonardo compatible
K-type thermocouple
USB powered

## Slide 7
5V, 600mA external relay
control capability
SD Card for Profile storage
Simple setup and operation
Open hardware design

## Slide 8
Controller
Toaster
Oven
Oven Power Control
USB Power
110 VAC
In
AC Power
AC Power
Relay Control
5v 600ma
Temp Probe

## Slide 9
Thermocouple
AC Power Switch
RefloLeo
Thermocouple

## Slide 10
SD Card
Profile Select
Profile Select
Start
Thermocouple
AC Power
Control

## Slide 12
Reflow Profile Command Examples
T130,000 Goto 130 degrees
W000,015 Wait 15 seconds (and turn off heat)
H150,120 Hold at 150 degrees for 120 seconds
T212,000 Goto 212 degrees
W000,020 Wait 20 seconds (and turn off heat)
X000,000 Exit program and turn off relay

## Slide 13
Profile 0 = Kester EP256 Solder Paste
Profile 1 = Hot Pocket Reheat
Profile 2 = Tuna Melt Sandwich
Profile 3 = Mini Pepperoni Pizza
Multiple Profiles Stored on the SD Card

## Slide 14
W6PQL
LED Meter

## Slide 15
W6PQL
LED Meter
Set for oven

## Slide 17
W6PQL
LED Meter
Fresh out
of the oven

## Slide 18
KT1VT Peaberry SDR

## Slide 19
W1GHZ Reference Switch all pasted up

## Slide 20
W1GHZ Reference Switch parts placed

## Slide 21
W1GHZ Reference Switch completed

## Slide 23
The Shop

## Slide 24
Board under the microscope ready for solder paste

## Slide 25
Yellow lines are where solder paste was placed

## Slide 26
First Attempt – Test Board

## Slide 27
Working Board

## Slide 28
Working Board
Rear View

## Slide 29
Wait for Solder Paste to come to room temp before use
There is a finite time for solder paste to sit before Reflo
If you start a board, plan on finishing it in one sitting
Preheat Oven at least once before use
For clean up and rework
TechSpray #2 size No Clean braid
Kester .015 No Clean 23-6337-8806 SN63PB37
For a toaster oven, get the smallest with the max heat
Mine is 1200 watt

## Slide 30
Reflow Master Pro on Tindie
$89

## Slide 31
QUESTIONS?
Surface Mount Assembly
with a Toaster Oven
Mike Seguin, N1JEZ
Eastern VHF/UHF/Microwave Conference 2024