## Slide 1: Very Low Noise Unconditionally Stable MMIC Amplifiers
Paul Wade W1GHZ

## Slide 2: Remember Building Preamps?
Exotic Device - $$$
Johanson Trimmers
Finicky construction
Tune until trimmers wear out
NF changes on antenna
Oscillates if bird flies by
 3 dB NF

## Slide 3: QST 1978 GaAsFET

## Slide 4: 2016 MMIC – PGA-103

## Slide 5: 2024 MMIC – NXP BGU8051 Uncondiotionally Stable

## Slide 6: NXP BGU8051 MMIC
Tiny Package – 2 mm square
No leads – pads under package
Ground pad under middle
Pad spacing 0.5 mm
Bias resistor to set current
Toaster 0ven soldering – N1JEZ

## Slide 7: Simple Schematic

## Slide 8: BGU8051 Performance

## Slide 9: Unconditionally Stability
Will not oscillate
Performance less sensitive to impedances
Rollet’s Stability Factor:

## Slide 10: Simple Stability Gain (S21) less than Isolation (S12)

## Slide 11: BGU8051 Noise Figure
Poor calibration at very low NF
Approximate NF based on comparison to previously measured units
144 MHz: ~ 0.25 to 0.4 dB
432 MHz: ~ 0.4 dB
1296 MHz: ~ 0.5 dB
Better measurement at conference

## Slide 12: Similar MMICs
Qorvo QPL9547 – needs bias resistor
Qorvo TQP3M9036 – no resistor
Qorvo TQP3M9037 – no resistor
All fit same preamp PCB
All Unconditionally Stable

## Slide 13: Comparison of 4 MMIC types

## Slide 14: Comparison of 4 MMIC types

## Slide 15: Comparison of 4 MMIC types
All have comparable Noise Figure up to 1296
QPL9547 and TQP3M9037 better gain to 3.4 G
This PC board not good at 5760

## Slide 16: Package
PC board fits in smallest Pomona box
Fits fine in small Altoids tin

## Slide 17: ebay module - TQP3M9037 LNA

## Slide 18: ebay module - TQP3M9037 LNA

## Slide 19: ebay module - TQP3M9037 LNA

## Slide 20: MMIC Preamps
Very low Noise Figure
Simple
Unconditionally stable
No tuning (you can try for better NF)
MMICs from Mouser - $3 to $5
PC boards available if there is interest
Toaster Oven soldering

## Slide 21: No tuning
No tune preamp
No tune SSPA
No tune transverter
Fixed calling frequency
Who needs a tuning tool?

## Slide 22
www.w1ghz.org