## Slide 1: IMD in Transmitter Circuits
WA1MBA
Tom Williams
2024 NEWS VHF Conference

## Slide 2: QUIZ
WHICH OF THESE IS A MIXER?
Marki
Microwave
Mixer
Rusty Nail
In Sheet
Metal
Coax
Connector
Corroded
Connection
Quality
LDMOS
Power
Amp
Pencil
On
Metal
Sample
And Hold
Circuit

## Slide 3: QUIZ
WHICH OF THESE IS A MIXER?
Marki
Microwave
Mixer
Rusty Nail
In Sheet
Metal
Coax
Connector
Corroded
Connection
Quality
LDMOS
Power
Amp
Pencil
On
Metal
Sample
And Hold
Circuit
* A Mixer is a Mixer

## Slide 4: QUIZ
WHICH OF THESE IS A MIXER?
Marki
Microwave
Mixer
Rusty Nail
In Sheet
Metal
Coax
Connector
Corroded
Connection
Quality
LDMOS
Power
Amp
Pencil
On
Metal
Sample
And Hold
Circuit

## Slide 5: QUIZ
WHICH OF THESE IS A MIXER?
Marki
Microwave
Mixer
Rusty Nail
In Sheet
Metal
Coax
Connector
Corroded
Connection
Quality
LDMOS
Power
Amp
Pencil
On
Metal
Sample
And Hold
Circuit
Dissimilar metals and oxides
Create RF diodes

## Slide 6: QUIZ
WHICH OF THESE IS A MIXER?
Marki
Microwave
Mixer
Rusty Nail
In Sheet
Metal
Coax
Connector
Corroded
Connection
Quality
LDMOS
Power
Amp
Pencil
On
Metal
Sample
And Hold
Circuit
Dissimilar metals and oxides
Create RF diodes

## Slide 7: QUIZ
WHICH OF THESE IS A MIXER?
Marki
Microwave
Mixer
Rusty Nail
In Sheet
Metal
Coax
Connector
Corroded
Connection
Quality
LDMOS
Power
Amp
Pencil
On
Metal
Sample
And Hold
Circuit
Non-linear devices mix signals

## Slide 8: QUIZ
WHICH OF THESE IS A MIXER?
Marki
Microwave
Mixer
Rusty Nail
In Sheet
Metal
Coax
Connector
Corroded
Connection
Quality
LDMOS
Power
Amp
Pencil
On
Metal
Sample
And Hold
Circuit
Ferrous metal in an RF
path can be non-linear

## Slide 9: QUIZ
WHICH OF THESE IS A MIXER?
Marki
Microwave
Mixer
Rusty Nail
In Sheet
Metal
Coax
Connector
Corroded
Connection
Quality
LDMOS
Power
Amp
Pencil
On
Metal
Sample
And Hold
Circuit
Switches are Mixers
(the extreme case of
Nonlinearity)

## Slide 10: Mixers are Nonlinear Devices the best of which are high speed switches
Designed and Intended Mixers
Nonlinearities in / from
  Diodes including
    Packaged Diodes
    Corroded connections
  Transistors
    Bipolar
    FET (MSEFET, LDMOS, etc)
  Ferrous material in the RF path
Switches (if switched at an LO frequency)

## Slide 11: Inter Modulation Distortion
A distortion caused by the MIXING of frequencies which are not intended to be mixed

## Slide 12: Inter Modulation Distortion
Lower, more negative numbers are better, expressed as -XXdBc
-80 dBc
-20 dBc
INPUT
OUTPUT

## Slide 13: Inter Modulation Distortion
A distortion caused by the MIXING of frequencies which are not intended to be mixed
Every mixer will mix every signal and create what we call IMD Which are products we don’t want
Reduction of unwanted mixing products is the same as reduction of IMD - BUT
  The difficult products are those in and around the transmitted signal, and cannot be filtered
  So the only way to reduce them is to prevent or reduce their generation

## Slide 14: Hold on – mixing those two 222 MHz frequencies will make products way up at 444 MHz and down near DC – What gives?
1,300 Hz
1,300 Hz
1,300 Hz
1,300 Hz
1,300 Hz

## Slide 15: Now Billy, this is your exam for 8th grade Arithmetic. What Mixing Products are in the Passband?

## Slide 16: It’s really Much Simpler
Mixers generate not only LO + IF and LO – IF (generally what we want) but also 2xLO+IF, 2xLO – IF, 2xLO + 2xIF, 2xLO-2xIF, and so on.
    Given a 700 Hz and a 2000 Hz tone USB at 222.100 MHz
    One of the products is (2xLO+2xIF2) - (LO+F1)
    (2xLO+2xIF2) is 2x194 =388 + 56.2040 = 444.2040 MHz
    (LO+F1) = 194 + 28.1007 = 222.1007 MHz
    The product is 444.2040 – 222.1007 = 222.1033
    222.1033 is 1300 Hz above the IF2 signal at 222.1020
    Similar arithmetic generates all the IMD tones at 1300 Hz spacing

## Slide 17: SPOILER ALERT – NO MOREMATH

## Slide 18: Typical (bad) VHF Transmitter Chain
Amps, Mixer, LO, Gain, Filters, Amplifier
WA1MBA PRESENT STATION
FLEX Transceiver, Old DEMI Transverter, Mirage AMP
-12 dBc SSB is bad, and that is running at ½ power
Transceiver
Transverter
Amplifier
Filters,
Coax, Ant
28 MHz
+0dBm
1 milliwatt
IMD almost
Unmeasurable
-80dBc
222 MHz
+40dBm
10 Watts
IMD
-14.5
Capable of
20 W
222 MHz
+47dBm
50 Watts
IMD -12 dBc
Mr. Splatter
Capable of
100W
Frequency
Power dBm
Power Watts
IMD dBc
Can it be worse?

## Slide 19: 2 Things to Reduce IMD
Properly Terminate Mixers (ALL MIXERS)
Operate all devices, especially including Power Amplifiers in their Most Linear Region

## Slide 20: To reduce unwanted mixer products properly terminate IF and RF ports
Minicircuits makes a few such filters for some IF frequency ranges, including 28 MHz
Had to make my own for the RF port 222 MHz
I am not a great RF Filter Designer, so took a simple filter approach

## Slide 21: Constant Impedance Filter A

## Slide 22: Construction

## Slide 23: Cascading Filter A

## Slide 24: Getting it to work

## Slide 25: Cascading and Tuning did OK

## Slide 26: Constant Impedance Filter B

## Slide 27: Built

## Slide 28: Cascading Filter B

## Slide 29: Getting it to work

## Slide 30: It worked OK but not Great

## Slide 31: Constant Impedance Filter C Diplexer (with load)

## Slide 32: Diplexer/Constant Impedance High Power Filters
QEX July/August 1999, William Sabin W0IYH (SK)

## Slide 33: FLEX Power Genius HF PA

## Slide 34: Design of HPF

## Slide 35: Build a nice high power HPF
SEE THE PRETTY NPO 3.6KV 10 AMP CAPS? $$
SEE THE PRETTY SILVER WIRE? $$
SEE THE HAM WIHTOUT AN ENGINEERING DEGREE?
PARASITICS SWAMPED THE CIRCUIT, NO GOOD.

## Slide 36: That was 2 days ago
Not working yet
Probably have to design both HP and LP together (a “contiguous diplexer”)
Found that parasitics – primarily capacitance –were overwhelming the as-built
So, a lot more to do
Anyway, I have some filters to play with in test circuits

## Slide 37: So Much for Filters How about Linearity?

## Slide 38: LDMOS Power Amplifiers
N4GA – Bob Go to: n4ga.com
  Avoid power levels into compression
  Operate at AB or A. Try 1 AMP per device idle current (1 Amp each side of a dual part) but possibly increase up to 4 Amps each side
  Note – that is 100 to 400 Watts of IDLE POWER
  Push Pull amplifiers, so have to Balance Idle Current for MINIMUM EVEN HARMONICS
  Stabilize Bias Current (over temperature)
  RUN at high voltage (e.g. 50V not 48V)

## Slide 39: N4GA Bias Board

## Slide 40: WA1MBA Filter - not a new idea
Trying a (high power) Constant Impedance Filter – Just like Broadcast Transmitters and the FLEX Power Genius HF PA “Harmonic Load”
Put it on output of PA, between PA and LP Filter
Prevents harmonics and other products reflecting back into amplifier from LP Filter
Reduces unwanted PA mixing products – IMD – just like a constant impedance filter on a mixer IF and RF port reduces IMD

## Slide 41: Firsts – the Test Setup
Built a 2 tone generator (audio in to FLEX 6700)
Built a 222 up-converter, 28 MHz in at 0 dBm, output 7 to 15 W sufficient to drive a KW class LDMOS amplifier
  Made a diagram, found a bunch of standard amplifiers (mostly Minicircuits), a Mixer, a bunch of filters, included couplers to sample signals
  Built some filters
Performed experiments

## Slide 42: Observations
Getting signal levels right and adjustable, and making repeatable measurements is a bear
Some low level gain blocks have fairly poor IMD performance, some have excellent
No amplifier produced better than -30dBc IMD (military, not ARRL dB) when driven beyond 6 dB below P1dB compression point.
  That means ¼ of the “rated power” - INCLUDING
  $600 60 – 300 MHz 10 watt Minicircuits amplifier
  Q5 Signal 25 watt 222 amp

## Slide 43: Circuit
30 MHz
BPF
ATT
PIF 30
DigiLO
194
MHz
Fixed
Atten
IF
LO
RF
Transceiver
28 MHz 0 dBm
IMD at least -80 dBc
10 MHz Ref
MBA Dual +
DEMI SAW
MCL 3011
MCL
ZHL03-5
Fixed
Atten
ATT
Q5 25 W
222 Power Amp
Mixer IF input
28 MHz -3 dBm
IMD -69 dBc
Mixer RF output
222 MHz variable
-31 to -10 dBm
IMD -60 worst case
Driver RF output
222 MHz variable
+1 to +20 dBm
IMD -55 to -44 dBc
RF Power output
222 MHz variable
+23 to +42 dBm
IMD -49 to -17 dBc

## Slide 47: Driver Amp Results

## Slide 48: 25 W Power Amp Results

## Slide 49: Results
It was possible for me to build an upconverter that produced 7 watts at -35dBc IMD*
  Filtered the Mixer IF port using a Minicircuits PIF-30 constant impedance filter
  Filtered the Mixer RF port using two home brew constant impedance filters followed by a DEMI 222 BPF (SAW filter)
  Adjusted signal levels throughout system so that could vary final power up to full 25 watts while maintaining drive to that final amplifier at -40 dBc IMD*

## Slide 50: Results
Working on 222 power amp – didn’t finish construction in time for conference
Just finished first version of diplexer, of course, it needs to be designed better, then tuned
Hope to complete next steps before CSVHF
However, did add a “line stretcher” to output of 25 W amp into LPF and load, and could affect IMD at 10 watts by nearly 3 dB by changing phase of reflected harmonics

## Slide 51: Recommendations
If you are designing any circuit which is going to be transmitting SSB or AM (and therefore want to limit unnecessary IMD)
  Try to make it as linear as you can
  If you are not able accurately measure IMD, keep the output level 7 dB below the P1dB point
  Try to terminate all ports properly (50 Ohms) at all frequencies from the lowest to at least 3 times that

## Slide 52: And, there is plenty of Receive IMD
Overdriven LNAs
Overdriven transverter amplifiers
Overdriven Mixers
Improperly terminated amplifiers and mixers
Unless you know your signal limits when IMD starts, don’t blame your local station for transmitting it
To test, turn your antenna and watch the unwanted components on your spectrum scope and waterfall
  If the relative heights between unwanted (out of normal bandwidth) products and peaks stay the same, it is the transmitter.
  If they change its at least partly your receiver

## Slide 53: Don’t be like Me -12 dBc = Mr Splatter Fortunately, I often use CW & Crank it up to 100 W

## Slide 54: FYI - I do POTA sometimes, and like CW

## Slide 55: Let’s sequence, I’ll TX on Even