## Slide 2
SDR Advances and the Future of SDR
  April 18, 2015 Phil Theis, K3TUF
Engineering, PennSun Solar
FLEXRADIO SYSTEMS

## Slide 3: SDR Advances Agenda
What is an SDR?
New Technologies in SDR
  Direct Sampling
  SmartSDR Architecture
  Networking
  CESSB
  Wide and Narrow simultaneously
Future SDR Capabilities

## Slide 4: Is this radio an SDR?
Modulation: FM Only
Change Controls? No
Change Functions? Yes
User programmable? Yes
Software controlled? Yes

## Slide 5: Is this radio an SDR?
Modulation: Fixed set
Change Controls? No
Change Features? Theoretically...
User programmable? No
Software controlled? Yes

## Slide 6: Is this radio an SDR?
Modulation: expandable
Change Controls? Yes
Change Features? Yes
User programmable? Yes
Software controlled? Yes

## Slide 7: What is Software Defined?
Modulation using software, changeable YES
Digital Signal Processing in software YES
Control Surface Reconfigurable YES
Can add new feature with new control YES
Radio controlled by software YES

## Slide 8: Yes, yes, but: BENEFIT?
What has SDR done for you lately?
  New mode?
  New feature?
  New controls?
  New capabilities?
If not, who cares if it’s called SDR?
I WANT
SDR
BENEFITS

## Slide 9: RF Tracking Notch Filter™
New control
New display
New DSP
(inside)

## Slide 10: Radio RF/IF Architectures
Multi-conversion a.k.a. superheterodyne
  Your car radio, your TV, any older scanner you have
  Most every Kenwood, Icom, Ten-Tec, Elecraft and Yaesu on the market today
Direct Conversion
  FLEX-5000, FLEX-3000, FLEX1500, Elecraft KX3
Direct Sampling a.k.a wideband
  FLEX-6000, HPSDR

## Slide 11: Multi-Conversion
RF Spectrum
64.455 MHz
455kHz
36kHz
DSP
DET
3–15 kHz
Roofing Filter
ADC
96ksps
On the IC-7600:
“When compared to a typical triple-conversion system, the double conversion system is more difficult to implement but it dramatically reduces signal distortion and provides a high-fidelity RF signal to the DSP processor.”
— Icom America website
Distortion

## Slide 12: Direct Conversion
RF Spectrum
192kHz
DSP
DET
FLEX-5000
ADC
DET
PAN
192ksps
Distortion

## Slide 14: Direct Sampling
RF Spectrum
245.76MHz
DSP
DET
FLEX-6000
ADC
DET
PAN
DET
122.88MHz
245.76Msps
There are still mixers and filters, but they are all math and “perfect” in DSP

## Slide 15: Direct Sampling Benefits
+ Distortion minimized (ADC @ antenna): best signal clarity
+ n-Receivers, n-Panadapters and varying widths see more bands, more receivers
+ Extremely high dynamic range: operate in worst conditions
+ Extreme flexibility through reprogrammability (ultimate SDR): future benefits
– Technically challenging to design

## Slide 16
We are called to be the architects of the future, not it’s victims
—R. Buckminster Fuller

## Slide 17: Design Options: #1: ADC and a hose
Radio is ADC ⟹ FPGA ⟹ Ethernet
Leverage PowerSDR; minimal SW investment
ADC
FPGA
PC
RADIO

## Slide 18: ADC and a hose: CDRX-3200
CDRX-3200, circa 2008
32 Synchronous, Coherent ADCs + FPGA
440Mbps bandwidth
Our customers have trouble absorbing the bandwidth

## Slide 19: ADC and a hose: LBRX-24
LBRX-24, circa 2010
24 Microwave ADCs + 2 FPGAs
40Gbps bandwidth, yes Gigabit, 4x10Gb SFP+
Our customers’ PCs have memory in the 100s of GB

## Slide 20: Design Options: #2: ADC + FPGA + DSP/uP
RADIO
Radio reduces bandwidth to minimum before Ethernet
Oh gosh: start over with SW: big investment!
ADC
FPGA
PC/
OTHER
CHL
BB
DSP

## Slide 21: IN or OUT of the box?
OUT OF THE BOX (DSP in external PC)
+ Simpler, cheaper radio design: apparent cost benefit
+ Radio designer can shed software costs: “not my problem --- check with the community”
– Long term maintenance?: will volunteers maintain?
– Must buy a PC: Loss of some cost benefit
– Interoperability issues (PC - radio): computer knowledge important
– Architectural: Built only for local LAN / fast computer
IN THE BOX
+ : best signal clarity
+ n-Receivers, n-Panadapters and varying widths see more bands, more receivers
+ Extremely high dynamic range: operate in worst conditions
+ Extreme flexibility through reprogrammability (ultimate SDR): future benefits
– Technically challenging to design

## Slide 22: IN or OUT of the box?
IN THE BOX (DSP in radio)
– Complex design: time to market / cost disadvantage
– Processing Fixed: can’t just add new computer
+ Completely integrated: Radio vendor controls and can fix all issues
+ Architecture: Huge bandwidth advantage (think remote)
+ Porting easy: Run on many platforms quickly
+ Flexibility: Doesn’t preclude external DSP
+ Simplicity: Plug in, turn on and go
IN THE BOX
+ : best signal clarity
+ n-Receivers, n-Panadapters and varying widths see more bands, more receivers
+ Extremely high dynamic range: operate in worst conditions
+ Extreme flexibility through reprogrammability (ultimate SDR): future benefits
– Technically challenging to design

## Slide 23: Direct Sampling Radios
HPSDR
Hermes
HPSDR
RF DSP
DSP CTRL
ANAN-100D

## Slide 24: Direct Sampling Radios
RF DSP
CTRL
FLEX-6000

## Slide 25: Integrating the Baseband Processor Key Benefits
Consistent performance independent of PC
Minimized network bandwidth (think remote)
Minimization of “system” problems
Self-contained, rapid startup platform
Spectrum displays (panadapter) independent of available network bandwidth
Network optimized

## Slide 26: Spectrum Display BW
1MHz
<500kbps
1500:1
Bandwidth
Difference
10MHz
770Mbps

## Slide 33: Networking
EVERYTHING is moving to the network.
You can TAKE YOUR FUN WITH YOU

## Slide 34: What is a contact?
You’re at your QTH and you work Christmas Island
T32C
RF

## Slide 35: What is a contact?
You’re trade emails with the operator of T32C on Christmas Island. His email says “You are 599 here!”
T32C
RF
Internet

## Slide 36: What is a contact?
You talk to Christmas Island using your local 2m repeater and EchoLink
T32C
RF
Internet

## Slide 37: What is a contact?
You’re at the store and you remote control your home station to work Christmas Island
T32C
RF
Internet

## Slide 38: Does your radio need THIS?

## Slide 39: Does your radio run HERE?

## Slide 40: T/F: Rare DX is convenient Where’s your operating position?

## Slide 41: Adaptive Predistortion
Power Amplifiers: Nonlinearities
Designs have improved
What if we knew in advance of the PA?
Could we correct?
HPSDR: Pure Signal

## Slide 42: Predistortion Before

## Slide 43: Predistortion After

## Slide 44: Phase Noise
Affects both RX and TX interference capabilities
Oscillator phase noise getting better every year
Direct Sampling radios demanding
Take a look at the all FLEX-6000 Thunderbird FD

## Slide 45: Low Phase Noise Field Day

## Slide 46: Low Phase Noise Field Day
100W PSK31

## Slide 47: Speech Processor (CESSB)
David Hershberger, W9GR, approached us at Dayton 2013
Algorithm implemented in SmartSDR + on-air testing
Excellent speech and a ~2.5dB power improvement
Results and algorithm to be published in QEX later this year

## Slide 48: Speech Processor Power

## Slide 49: Many data streams at once
FLEX-6700
  8 narrow-band 24kHz receivers
  8 panadapters
  4 wide-band (192kHz) I/Q streams for skimming

## Slide 50: Multi-mode Waterfall

## Slide 51: Waterfall plus Bandscope

## Slide 52: CW Skimmer x4

## Slide 53: Digital Modes

## Slide 54: More Functional Displays

## Slide 55: WSPR times 4!

## Slide 56: EasyPAL

## Slide 57: TX6G: A Picture is worth 1,000 words

## Slide 58: The Future: Decoding
Today: CW, PSK, RTTY
Tomorrow: Everything Digital and voice
Digital is fully integrated … no cables

## Slide 59: The Future: Decoding

## Slide 60: The Future: Remote
Today: Mostly hacked together and inconvenient
Tomorrow: Easy remote, tablets everywhere

## Slide 61: The Future: Integration
Today: On premise integration driven by contesters
Tomorrow: Integration driven by plethora of remote solutions and the need to drive other hardware

## Slide 62: The Future: Signal Classification
Today: Virtually none
Tomorrow: Radios will find and classify signals (determine mode)

## Slide 63: The Future: Steering and MIMO
Today: Phased receive arrays, few TX arrays
Tomorrow: Every antenna will have an SCU and for operators with multiple antennas, instant arbitrary, rotation will be possible

## Slide 64: The Future: Visualization
Today: Panadapters, Waterfalls and the occasional scope
Tomorrow: New displays that show perspectives of data not previously seen. Operational advantage will drive innovation

## Slide 65: The Future: Noise Reduction
Today: Advanced NB, NR techniques in many radios
Tomorrow: Dedicated noise receivers will be used to eliminate noise more effectively, optimal combining across multiple antennas will emerge

## Slide 66: The Future: Networking
Today: Occasional Remote-to-base operation
Tomorrow: Remote assets will be combined inside of a single program to enhance operational capabilities. Remotes may be used in combining, DFing or other applications