## Slide 1: Experiences building the W6PQL 220 and 1.2GHz SSPAs
Or: How I learned to stop worrying and just built the darn thing

## Slide 2: The Journey
Barefoot in the park
Another Brick in the wall
Time to go for the Nuclear option

## Slide 3: W6PQL VHF and Up Amps & Modules
SSPA Modules
  1Kw to Legal Limit
    6m, 2m, 220, 432
  903, 1296, 2304
  Assembled, Modules, Kits & Boards
  Devices

## Slide 4: W6PQL VHF and Up Amps & Modules
Support Components
  Controller
  FET Switches
  Couplers, detectors & Filters
  Displays

## Slide 5: Building the SSPA Pallets
Build input board
  Extra pads in bias area are handy
  Resistor changes depending on device chosen
Build the output Board
  Follow order!
  No tie for VDD
  Transformers & Baluns are easier than you think
  You will need a hefty soldering iron
Test fit to heat sink
  Some adjustment may be required
Install device and test
Time to Complete: 2-3 Hours

## Slide 6: Testing the SSPA Pallets
Before you power up – install current limit And Clean up the workbench!
Instrument everything
  Volts & Amps on VDD and Bias
  FWD/REV Power on in and out
  Use A Solid dummy load
    Cantenna isn’t as bad as you think below 432!
    100W load in cold water
  Set bias
  Change current limit to high power
  Final Test
  Set it aside

## Slide 7: Time for the boring work Or: the remaining 90% of the work
Enclosure
  Desk or rack mount?
  Air or liquid cooled?
Support Circuitry
  Controller, switches, filters, relays, metering
Power supplies
  Self contained or shared?
cabling
Notes: Pallets will fit in a 2U enclosure

## Slide 8: Amp Controller
Build or buy a controller?
Requirements
  Sequencer for relays, bias, ALC/RF Holdoff
  High Swr lockout
  Cooling control
  Blinky lights (Indicators)
Bonus
  High Temp lockout
  Temperature based fan control
  12V power output (12v-50v in
Time to complete: 2-3 Hours

## Slide 9: Additional Support
RF Metering
Vdd metering
Input Directional Coupler (ALC)
FET Switch for VDD
26Vdc power regulator
Time to complete: 1-2Hours

## Slide 10: Filter / Coupler
Kit or assembled?
Trust or Tune?
PQL Board 6-432
1296
  Build the filter
  Use Commercial coupler and W6PQL detector
Time to complete (including tuning): 2 hours

## Slide 11: Enclosure (layout)

## Slide 12: Enclosure
Build, buy, recycle?
Rack or desktop?
Power Supply or not?
Cooling plan
Time to complete:
  Assembly
  Cabling
  Customization
  ~10 hours

## Slide 13: Enclosure

## Slide 14: Enclosure

## Slide 15: All the Other things you’ll end up ordering…

## Slide 16: All the Other things you’ll end up ordering…
Switches
Connectors
Cable
hardware